## Slide 1
Operational monitoring of thermal hotspot events with the Sentinels by EUMETSAT Central Facility
Edouard Martins, Julien Chimot, Oscar Henriquez, Andrea Meraner, Rasmus Lindstrot, Bertrand Fougnie, Bojan Bojkov (EUMETSAT)
EUMETRAIN - Event week on Forest Fires (1-3 June 2026)

## Slide 2
What is EUMETSAT?
Copernicus Sentinel-3
Monitoring thermal hotspots with Sentinel-3 satellites
And Sentinel-4 and Sentinel-5?
Outcome

## Slide 3: What is EUMETSAT?
GREECE
ITALY
IRELAND
ICELAND
HUNGARY
AUSTRIA
CZECHIA
CROATIA
BULGARIA
BELGIUM
SPAIN
UNITED KINGDOM
TURKEY
SWITZERLAND
SWEDEN
POLAND
SLOVENIA
SLOVAK REPUBLIC
ROMANIA
PORTUGAL
DENMARK
GERMANY
FRANCE
FINLAND
ESTONIA
LATVIA
NORWAY
THE NETHERLANDS
LUXEMBOURG
LITHUANIA
User-driven intergovernmental organisation based in Darmstadt (Germany)… turning 40 years this year 🎂
Main objectives: Establish, maintain and exploit European systems of meteorological satellites (GEO+ LEO satellites) Contribute to the operational monitoring of the environment, climate and detection of global climatic changes
Main users: Numerical Weather Prediction centres, Assimilation centres (ECMWF, NOAA), Copernicus services Other operational organizations (ESA, NASA, etc.), Academia, etc.
For Fires topic: EUMETSAT Central Facility = Copernicus FRP
LSA-SAF = GEO + EPSSG FRP
EUMETSAT: EUropean organisation for the exploitation of METeorological SATellites (intergovernmental organisation with 30 Member States)

## Slide 4: EUMETSAT’s current and future missions
JASON-2 2009
Sentinel-3A 2016
JASON-CS/ SENTINEL-6 2021
JASON-3 2016
Metop-B 2013
Metop-C 2018
Metop-SG A
Sounding & Imagery 2025/26
Metop-SG B
Microwave Imagery 2026
Sentinel-5
on Metop-SG A 2025/26
Sentinel-4
on MTG-S 2025
MTG-S
Sounding 2025
MTG-I
Imagery Dec. 2022
MSG-4 / Meteosat-11 In-Orbit Storage 2016
Prime Satellite 2018
Meteosat-10
2013
Meteosat-9
2006
Sentinel-3B 2018
Geostationary
Programmes
Polar
Programmes
Mandatory
Programmes
Optional and
Third Party
Programmes
(incl. Copernicus)
CO2M
2026/27
4

## Slide 5: EUMETSAT Central Facility
Entrusted by EUMETSAT Member States & Copernicus – GEO + LEO satellites!
Expertise support regularly provided to operational air quality & climate services with ECMWF
  Primary needs are both air quality / population health / aviation & security + land surface monitoring
All Developments, Calibration, Validation, and Evolutions directly led in-house and/or with LandSAF supported by key European expertise hired on dedicated topics – NRT (<< 3h), 7/7 days, 24h led by EUMETSAT operators & System Engineers.
European NRT satellite Fires providers
Fire
User Communities
MSG/SEVIRI
Copernicus
Sentinel-3 NRT
MTG-I/FCI
EPS-SG/MetImage
1st European NRT satellite Fires
(2009-present)
Led by LSA-SAF
2nd European NRT satellite Fires (2020-present)
Led by EUMETSAT CF
3rd European NRT satellite Fires
(2025-present)
Led by LSA-SAF
Copernicus Sentinel-4 (onboard MTG-S) & Sentinel-5 (onboard EPS-SG)
Via the tracking of smoke plume, chemical composition, and air quality impacts
Led by EUMETSAT CF
Copernicus Sentinel-3 New Generation Optical

## Slide 6
What is EUMETSAT?
Copernicus Sentinel-3
Monitoring thermal hotspots with Sentinel-3 satellites
And Sentinel-4 and Sentinel-5?
Outcome

## Slide 7: Copernicus Sentinel-3
EUMETSAT is entrusted by European Commission and Copernicus to provide the Near Real Time (NRT) Atmospheric Products from Sentinel-3 (currently: Aerosols, Fires, Atmospheric Vectors, soon: Water Vapor)
Launches: Sentinel-3A (2016) and 3B (2018) … (3C in Q3 2026; 3D in 2028)  20+ years of mission continuity
  SLSTR : Sea and Land Surface Temperature Radiometer  observations used to derive NRT Fire Radiative Power (FRP) product
Sentinel-3
SLSTR
OLCI
MWR
SRAL

## Slide 8
What is EUMETSAT?
Copernicus Sentinel-3
Monitoring thermal hotspots with Sentinel-3 satellites
And Sentinel-4 and Sentinel-5?
Outcome

## Slide 9: But first, a satellite picture with our eyes…
https://s3view.oceandatalab.com
Sentinel-3 A+B, OLCI, 19.08.2020 – A normal day?

## Slide 10: Sentinel-3 monitoring Sentinel-6 Ground antenna threaten by fires
Day-time SLSTR NRT Active Fire detection (Coll 3.1)
OLCI RGB imagery
Fire Radiative Power [MW]
Alaska, Fairbanks – 5th July 2025

## Slide 11: Detecting Wildfires with Sentinel-3 in NRT (mandate EC)
Original algorithm by M. Wooster (King’s College London – KCL)
- Collection 1 (2020) – Operational Nighttime
  - Collection 2.0 (2021) – Demonstrational Daytime
  - Collection 2.1 (2022) – Pre-operational Daytime
Precursor “Day1”
Currently “Day1.5”
Incremental evolutions by EUMETSAT CF of the operational processor to derive NRT FRP for:
User needs and requests
Upgrade product quality and user-friendliness
Collection 3.0
Collection 3.1
July 2024
mid-June 2026
Operational Daytime MWIR
Comprehensive enhanced user-friendliness of the format  creating mini-csv and mini-netcdf files
Fixed anomaly on
SZA derivation
January 2025
Collection 3.2
launch S3C
September 2026
Improved detection accuracy of MWIR hotspots
using subpixel information (see next slides)
New fire confidence classes
Implementing ‘fire-free’ clear-sky land mask
for supporting the assimilation of the product for weather smoke
Enhanced VIS/SWIR calibration
TODAY

## Slide 12: Preparing transition from MODIS/Terra (NASA) to S3 (Europe)
Portugal/Spain fires - August 2025
FRP [MW]
Wildfire peak Portugal / Spain
S3 NRT
AOT(550 nm) (Coll3.1)
-------- S3A+B (Coll3.1)
-------- MODIS (Coll6.1)

## Slide 13: GEO-LEO match-ups for S3 NRT FRP product
GEO – LEO match-up inter-comparison => Evolution towards MTG-FCI.
Overall, like with MODIS inter-comparison since 2020: high confirmation of a very large number of small (weakly radiative) fires additionally detected by Sentinel-3 during night-time. Benefits from:
  SLSTR instrument Field Of View
  Original KCL algorithm (Wooster et al., 2012; Xu et al. 2021)
Mean Absolute Difference FRP:
19MW (Day) ; 7MW (Night)
Credits: Andrea Meraner (EUMETSAT)

## Slide 14: Upcoming Collection 3.2 (continue addressing challenges related to false alarms)
The operational processor is in constant evolutions to take into account
  Improvement of known limitations
  Fulfillment of user requests and needs
Upcoming Collection 3.2
  Continuing enhanced and comprehensive user-friendliness (format and size of the product)
  Improving accuracy of hotspot detection (see next slides)
  Better user guidance by revising detection confidence
  Adding fire/non-fire flags to support smoke weather assimilation
Coll3.1 (OPE)

## Slide 15: Coll3.2 - Removing known False alarms in Daytime
Adding new rejection tests for bright reflective targets in Daytime (based on thresholds on Red-NIR-MWIR)

## Slide 16: Coll3.2 - New confidence classes for better user guidance
black cells = 500m image grid (S1S6)
orange cells = 1km image grid (S7S9; F1)
Use of subpixel information within the 1km MWIR IFOV 500m grid (for VIS+SWIR) and 1km grid (for MWIR)
‘Lower’ confidence (=0) | if confidence_level < 30% or flag(bright_targets) is raised or flag(cloud_edges) is raised
‘Nominal’ confidence (=1) | if 30% < confidence_level < 80%
‘Higher’ confidence (=2) | if confidence level > 80%

## Slide 17
What is EUMETSAT?
Copernicus Sentinel-3
Monitoring thermal hotspots with Sentinel-3 satellites
And Sentinel-4 and Sentinel-5?
Outcome

## Slide 18: Fire emissions
Biomass burning is one of the main sources of trace gases and aerosols in the atmosphere and significantly affects its chemistry and radiative balance. Increasingly devastating wildfires have impacts on air quality and the climate.
The list of trace gases emitted by fires is long and includes, for example, carbon monoxide, formaldehyde, glyoxal, etc., which can also be measured by satellites.
S5P/TROPOMI carbon monoxide mixing ration, weekly average (Borsdorff et al., GRL 2018).
S5P/TROPOMI Glyoxal, September 2020 (BIRA)

## Slide 19: Sentinel-4 and Sentinel-5
Together, both S4 and S5 missions provide complementary data, enabling regional & global insights into air quality and atmospheric conditions.
Sentinel-5/UVNS onboard EPS-SG (LEO, launched in August 2025)
Sentinel-4/UVN onboard MTG-S (GEO, launched in July 2025)
spatial resolution: 7*7km pixels,
sun-synchroneous orbit 9.30 am/pm
spatial resolution: 8*8km pixels,
throughout the day in Europe
Credits: R. Lindstrot (EUMETSAT)

## Slide 20
What is EUMETSAT?
Copernicus Sentinel-3
Monitoring thermal hotspots with Sentinel-3 satellites
And Sentinel-4 and Sentinel-5?
Outcome and conclusion

## Slide 21: Copernicus Sentinel-3 NRT L2 Aerosol & Fire suite
NRT L2 Atmospheric products from S3 solely entrusted to EUMETSAT CF by the European Commission (EC), part of the Copernicus Program
Operational & available in << 2.5h (since sensing time), with increasing timeliness under further developments (e.g. fast FRP).
Continuous incremental algorithm evolution, driven by operational user needs.
Collaboration across diverse teams including L1 calibration experts, operators and L2 aerosol / fire experts, supported by external partners.
Preparation of S3C commissioning and full-mission time-series reprocessing.
Intensive support to users including Copernicus services
(CAMS, CEMS) assimilating S3 NRT AOD / FRP since 2026.
L2 NRT Aerosols - Coll 3.1
L2 NRT Fires - Coll 3.1
Fire radiative Power (FRP) [MW]
Total AOT(550 nm)

## Slide 22: Access to S3 NRT FRP data
EUMETSAT Data Store (https://user.eumetsat.int/data-access)
EUMDAC library (via command line on terminal) https://user.eumetsat.int/resources/user-guides/eumetsat-data-access-client-eumdac-guide eumdac download –c EO:EUM:DAT:0417 –s YYYY-MM-MMThh:mm –e YYYY-MM-MMThh:mm –timeliness NR
(i.e., product ID of S3 NRT FRP = 0417)
For visualisation: EUMETView https://view.eumetsat.int/productviewer?v=default